H8 development kit brief introduction

H8 is based on Allwinner A80 SoC is released by Merrii, we can provide users with Android4.4.2 / inux3.4.39+qt and Lubuntu to develop board.

A80 Hummingbrid H8 is a mini board based on A80, there are two USB hosts, an 3.0 OTG, a Gigabit Ethernet , a WIFI/BT4.0 as well as line in and HDMI HD video output besidesVGA output, support 3G/4G. It has all the basic functions of a PC when connect TV and keyboard, such as preadsheets, word processing, play games and HD videos etc.

●Specifications Of A80 SoC

A80 Hummingbrid H8 based on Allwinner UltraOcta A80 processor. A80 processor enriched with interfaces, including HDMI，EDP，LVDS/RGB LCD， USB & GMAC.

A80 processor applies the UltraOcta core ARM big.LITTLE Cortex-A15/A7 structure, both efficient of the Cortex-A15 and energy-saving of Cortex-A7. Equipped with POWERVR G6230 GPU, which is not only improves the system performance, but also satisfy the excellent game compatibility.

In addition, A80 supports 4K*2K@30fps decoding，4K*2K@30fps coding and HD 1080p@120fps coding.

| CPU | Octa-core big.LITTLE ARM Cortex-A15/A7 |
| --- | --- |
| GPU | PowerVR 64core G6230 GPU |
|  | Comply with OpenGL ES 3.0/2.0/1.1 OpenCL 1.1 Direct 9.3 |
| Video | HD H.264 4k*2k@30fps video decoding |
|  | Multi-format FHD video decoding, including Mpeg1/2, Mpeg4 SP/ASP GMC, H.263, H.264 BP/MP/HP, VP8, WMV9/VC-1, Jpeg/Mjpeg, etc. |
|  | 264 High Profile 4096*2048@30fps、1080p@120fps or 720p@240fps encoding |
|  | 3840x1080@30fps 3D encoding/decoding, BD/SBS/TAB/FP supported |
|  | Comply with RTSP, HTTP,HLS,RTMP,MMS streaming media protocols |
| Display | Support multi-channel HD display |
|  | Integrated HDMI 1.4 transmitter with HDCP support |
|  | CPU/RGB/LVDS LCD interface |
|  | Support YPbPr/VGA |
| Camera | Integrated parallel and MIPI I/F sensor |
|  | Support 8/10/12-bit YUV/Bayer sensor |
|  | Support 5M/8M/12M/16M CMOS sensor |
| Memory | RAW NAND Flash controller with 72-bit ECC |
|  | DDR3/DDR3L/LPDDR3/LPDDR2 controller,up to 8G |
| Audio | Integrated digital audio interface |
| OS | Android 4.4.2 、linux3.4.39 |

Structure of A80

●Highlights Of A80

The main specifications of A80 UltraOcta -core mobile application processor are as following:

-octa-core big.LITTLE Cortex®-A15/A7 CPU structure
　　  -PowerVR G6230 GPU
　　  -H.265/VP9 1080P@30fps video playback	
　　  -H.264/VP8 4K*2k@30fps、1080p@120fps  or 720p@240fps video encoding.
      -3840x1080@30fps 3D codec, support BD/SBS/TAB/FP format
      - built-in HDMI, an LVDS, etc

- The highest 16 m CMOS sensor

- Through Google CTS test, GMS in the grant application

- support Android 4.4.2 operating system

Strong ability of high-definition video processing

A80 processor supports 4096*2048@30fps video playback，4096*2048@30fps video coding，1080p@120fps/720p@240fps video coding, provide users a better experience.

High level of integration

High level of integration has been one of the highlights of SoC products, A80 is no exception, the platform integrates an LVDS, HDMI, EDP to make the system design simpler and BOM cost more competitive, products to market more quickly.

●Software features

Driver support: LCD, Touch Screen, UART, Gigabit Ethernet, HDMI, EDP, etc

Support from emmc Flash, SD card startup guide.

Default Android4.4 system, and provide Linux 3.4 source code

Linux OS Features:

    - Linux version: linux 3.4

Android OS Features：

    - Android Version: android 4.4.2 and above

Description Of Hadware Interface

| Name | Description |
| --- | --- |
| CPU | Cortex-A15/A7 PowerVR G6230 |
| PMU | X-Power AXP806+AXP809 smart power management specialist ,accessible to 12Vpower adapter, battery, USB5V power input |
| DRAM | 4*16 Bits DDR3 into 64bit 2048M Bytes DRAM |
| Flash | SDIN7DU2-8G |
| TF card | Support up to 32G card memory, support card test |
| WIFI | Wifi BT two-in-one module |
| Ethernet | 10M/100M/1000M IEEE802.3，use Realtek RTL8211D/E RJ45 |
| USBHost/USBOTG | 1 个 USB OTG 3.0/2.0 ，2USB Host |
| Headphone | Support stereo headphone output/line in |
| HDMI output | HDMI v1.4， support 4k at the most |
| UART | Provide UART interface, TTL level |
| Keys | RESET，POWER_ON etc |
| IR | IR only supports infrared remote control |
| DC | 5V DC IN |

●Description of Extended PIN

CSI camera output(J11)

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | VCC-5V |  | 2 | CSI0-D2 |  |
| 3 | VCC-3V |  | 4 | CSI0-D3 |  |
| 5 | CSI0-PCLK |  | 6 | MIPI-CSI-SCK |  |
| 7 | MIPI-CSI-SDA |  | 8 | CSI0-VSYNC |  |
| 9 | CSI0-HSYNC |  | 10 | CSI0-MCLK |  |
| 11 | CSI0-D4 |  | 12 | CSI0-D5 |  |
| 13 | CSI0-D6 |  | 14 | CSI0-D7 |  |
| 15 | CSI0-D8 |  | 16 | CSI0-D9 |  |
| 17 | CSI0-D10 |  | 18 | CSI0-D11 |  |
| 19 | GND |  | 20 | GND |  |
| 21 | CSI0-D0 |  | 22 | CSI0-D1 |  |
| 23 | HUB_PWR_EN |  | 24 | GND |  |
| 25 | GND |  | 26 | TW2-SCK |  |
| 27 | UART-RX |  | 28 | TW2-SDA |  |
| 29 | UART-TX |  | 30 | SPI-CS0 |  |
| 31 | UART-RTS1 |  | 32 | SPI-CLK |  |
| 33 | UART-CTS1 |  | 34 | SPI-MOSI |  |
| 35 | GND |  | 36 | SPI-MISO |  |
| 37 | UART-RX1 |  | 38 | CSI-SCK |  |
| 39 | UART-TX1 |  | 40 | CSI-SDA |  |
| 41 | VCC-3V |  | 42 | MIPI-CSI-MCLK |  |

CON18					MIPI camera signal output

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | CSI-CLKP |  | 2 | CSI-CLKN |  |
| 3 | GND |  | 4 | GND |  |
| 5 | CSI-D2P |  | 6 | CSI-D2N |  |
| 7 | CSI-D0P |  | 8 | CSI-D0N |  |
| 9 | CSI-D3P |  | 10 | CSI-D3N |  |
| 11 | CSI-D1P |  | 12 | CSI-D1N |  |
| 13 | CSI-MCLK |  | 14 | CSI-SCK |  |
| 15 | CSI-RESET |  | 16 | CSI-SDA |  |
| 17 | CSI-PWDN |  | 18 | CSI-ID |  |
| 19 | VCC-IO-CAM |  | 20 | VDD-CAM |  |
| 21 | AFVCC-CAM |  | 22 | AVCC-CAM |  |

J4					LVDS signal output

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | VCC-LVDS |  | 2 | VCC-LVDS |  |
| 3 | VCC-LVDS |  | 4 | GND |  |
| 5 | GND |  | 6 | GND |  |
| 7 | LVDS0-D0N |  | 8 | LVDS0-D0P |  |
| 9 | LVDS0-D1N |  | 10 | LVDS0-D1P |  |
| 11 | LVDS0-D2N |  | 12 | LVDS0-D2P |  |
| 13 | GND |  | 14 | GND |  |
| 15 | LVDS0-CLKN |  | 16 | LVDS0-CLKP |  |
| 17 | LVDS0-D3N |  | 18 | LVDS0-D3P |  |
| 19 | LVDS1-D0N |  | 20 | LVDS1-D0P |  |
| 21 | LVDS1-D1N |  | 22 | LVDS1-D1P |  |
| 23 | LVDS1-D2N |  | 24 | LVDS1-D2P |  |
| 25 | GND |  | 26 | GND |  |
| 27 | LVDS1-CLKN |  | 28 | LVDS0-CLKN |  |
| 29 | LVDS1-D3N |  | 30 | LVDS1-D3P |  |

CON11					KEY external interface socket

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | GND |  | 2 | LRADC0 |  |
| 3 | UBOOT |  | 4 | RESET |  |
| 5 | POWON |  |  |  |  |

J6				Backlight inverter control interface

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | BL_IN |  | 2 | BL_IN |  |
| 3 | ON/OFF |  | 4 | ADJ |  |
| 5 | GND |  | 6 | GND |  |

J10				CTP Touch interface

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | GND |  | 2 | VCC_3V |  |
| 3 | I2C_SDA |  | 4 | I2C_SCK |  |
| 5 | TP_INT |  | 6 | TP_WAKEUP |  |

UART0-DEBUG interface

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | GND |  | 2 | VCC |  |
| 3 | UART0-RX |  | 4 | UART0-TX |  |

UART4

| Pin | Pin Name | IO type | Pin | Pin Name | IO type |
| --- | --- | --- | --- | --- | --- |
| 1 | VCC-3.3V |  | 2 | UART4-TX |  |
| 3 | UART4-RX |  | 4 | GND |  |

Prospect and Purpose

Due to the expansion interfaces of optimus development system are much

more than some other similar products, and it has got global high attention. Thus

making it very powerful, rich social environment and market value. The more people

participate, the more rapid development, the greater the potential market, followed

by the more purposes. Currently, besides the children's education above-mentioned,

it also can be used as basic computer, home theater HD player etc.

●Following uses:

• multimedia player

• PlayStation

• IPTV

• Emulation box

• Auto PC

• Car GPS

• smart robot

• Server

• Electronic Album

• remote surveillance

• Home alarm apparatus / automation system

Purchase

Contact person: Danielle

Tel：+86-755-86196321-808

Fax：+86-755-86196240

mobile：13322998873

Q  Q：2373876277

Email:  hd @merrii.com